SECTION 085677 – THERMAL WINDOW INSERTS

GENERAL

RELATED DOCUMENTS

Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to this Section.

SUMMARY

This Section includes the following:

Thermal window inserts.

SUBMITTALS

Product Data.

Shop Drawings: Submit shop drawings in detail of all work in scale to indicate size, location and attachment methods required for the installation of the required work.

Test Data: Submit tests establishing compliance with all performance characteristics of the specification.

QUALITY ASSURANCE

Manufacturer: The manufacturer shall have a minimum of three years experience in manufacturing window inserts and shall have completed at least five projects of the scope and quality required by this project.

The manufacturer shall have tested the window inserts for thermal values specified.

The manufacturer shall have complete installation drawings and instructions to insure a quality installation.

PRODUCTS

MANUFACTURERS/MASTER DISTRIBUTOR

Thermal Window Inserts:

Climate Seal a Division of Acoustical Surfaces, Inc. (Basis of Design)

123 Columbia Court North, Suite 201, Chaska, MN 55318.

952-448-5300, Fax: 952-448-2613.

Toll Free: 1-800-448-3134.

Or equal.

Master Distributor: Environmental Window Solutions, LLC. Charlotte, NC  28227.

704-200-2001, Fax: 704-973-9568.

Toll Free: 877-773-7379.

THERMAL WINDOW INSERTS

Product: Climate Seal Magnetic Interior Insulating Window System (Thermal Series) by Acoustical Surfaces, Inc.

Exterior grade magnetic PVC extrusion with impact resistance and U.V. stabilization for durability and strength.

3/4 inch wide x 7/8” inch Deep frame.

Receive up to 5/16 inch thick glazing.

Mitered Corners (except extreme out-of-square applications) to ensure maximum performance and sound abatement.

High performance “closed cell” thermal weather strip foam to further eliminate air infiltration between the primary window frame and the Climate Seal’s steel attachment angle.

Only 1/2 the weight of other glass manufacturers as a result of using either acrylic or polycarbonate glazing.

Trim: Dual durometer polyvinyl chloride extrusion with magnet trim incorporated.  Color to match window frame.

Size: As indicated on Drawings.

Mounting Methods: Surface or In-Jamb as indicated on Drawings.

Molding and Frame:

Standard: Factory extruded White or Dark Chocolate Brown as selected by Architect.

Custom: Wood veneer as selected by Architect. Custom painting or custom extrusion colors available (per a minimum Lineal Footage requirement).

Acrylic glazing/glass: Tinted, privacy, abrasion resistance, or museum quality UV filtering as selected by Architect.

American National Safety Glazing Standard ANSI Z97.1.

International Conference of Building Officials (ICBO).

Uniform Building Code (UBC).

UL Classifications; 94HB, HBE162, 746C, UV Light.

Thermal Performance Tests Data: ATI-2305 and ATI-2309. Based on a single pane primary window measuring 2’8” x 4’0.

U-Value:

Without thermal window insert: 1.15 BTU/HR FT2/FT.

With thermal window insert: 0.44 BTU/HR FT2/FT.

R-Value:

Without thermal window insert: .86.

With thermal window insert: 2.27.

CRF:

Without thermal window insert: 5.0.

With thermal window insert: 60.0.

R Value Increase with Preservation Window Inserts: Based on a single pane primary window measuring 2’8” x 4’0.

Single Pane Wood Window:

R value without thermal window insert: 1.12.

R value with thermal window insert: 2.38 (112% increase).

Single Pane Vinyl Window:

R value without thermal window insert: 1.09.

R value with thermal window insert: 2.33 (114% increase).

Single Pane Aluminum Clad Wood Window:

R value without thermal window insert: 1.11.

R value with thermal window insert: 2.27 (105% increase).

Single Pane Aluminum Window:

R value without thermal window insert: 0.91.

R value with thermal window insert: 1.92 (112% increase).

EXECUTION

EXAMINATION

Examine openings, substrates, structural support, anchorage, and conditions, with Installer present, for compliance with requirements for installation tolerances and other conditions affecting performance of work.  Verify rough opening dimensions, levelness of sill plate, and operational clearances.

Proceed with installation only after unsatisfactory conditions have been corrected.

INSTALLATION

Installer: The installer shall have a minimum of (5) five installation experience using Climate Seal magnetic window inserts (Certified Climate Seal Installer) or approved equal. If this qualification is not met and when applicable, a Certified Climate Seal Installer should be incorporated into the project to ensure order accuracy, proper installation techniques, etc.

Comply with Drawings, Shop Drawings, and manufacturer's written instructions for installing window inserts.

Install window inserts level, plumb, square, true to line, without distortion, anchored securely in place, and in proper relation to adjacent construction.

END OF SECTION 085677